## Slide 1: Example of the analysis and design of a bridge according to EC8/2
T. Isaković
UNIVERSITY OF LJUBLJANA
Faculty of Civil and Geodetic Engineering

## Slide 2
30 50 50 30
14
14
21
agR = 0,25g Soil C Bridge II. importance class
Ductile response
Deck cross-section
Concrete C35/45 E = 34 GPa
Steel B500
A = 9,65 m2 It = 36,5 m4
Asy = 3,82 m2 Iy = 96 m4
Asz =6,93 m2 Iz = 21,5 m4
According to EC8/2 It is reduced to It = 36,5/2 = 18,25 m4
S14
S21
S14

## Slide 3
Columns
40 120 40
200
40 270 40
350
C 25/30 E = 3,1∙107 kN/m2
A = 3,76 m2
Asy = 1,6 m2
Asz = 2,8 m2
It = 4,19 m4
Iy = 5,18 m4
Iz = 1,94 m4
h b h
y
z

## Slide 4
Box cross-section is favourable due to the large width of the compression zone, providing larger ductility
favourable
unfavourable

## Slide 5
S14
S21
S14
x
y
z
x
y
z
Coordinate systems
Actions
Dead load - superstructure g = 295 kN/m
Weight of piers gs = 94 kN/m
Masses
Bridge of II. importance class – only dead load is taken into account
Mass - deck Mp = g / 9,81 = 295 / 9,81 = 30 t/m
Mass - piers Ms = gs /9,81 = 94 / 9,81 = 9,6 t/m
Analysis

## Slide 6
Dead load
The axial forces occur in piers
Axial forces at the base of piers (weight of the piers is included)
NS14 = 14329 kN Normalized axial force
NS21 = 17485 kN Normalized axial force
Axial forces in piers are calculated using programme SAP2000

## Slide 7
Seismic analysis in the longitudinal direction
Fundamental mode method – Rigid deck model
Field of application:
a) Mass of piers less than 20% of the mass of the deck
Ms = (14 +21 +14) 9,6 = 470 t
Mp = 30∙160 = 4800 t Ms / Mp = 0,098
b) Eccentricity – Distance between the centre of mass and centre of stiffness is 0, the bridge is symmetric.

## Slide 8
SDOF model of the bridge
M
K
Total mass of the structure
M = 30∙160 + (7 + 10,5 + 7) 9,6 = 5035 t
Half of the piers‘ mass is added
Flexibility of piers
Stiffness of piers
Stiffness of the structure
K =2∙ks14 + ks21 = 144998 kN/m

## Slide 9
Design acceleration spectrum
ag = gI agR = 1∙ 0,25 m/s2 = 0,25 m/s2
Soil C:
S = 1,15
TB = 0,2 s
TC = 0,6 s
TD = 2,0 s
damping 5%
TC = 0,6 < T = 1,171 s < TD =2 s
q = 3,5
q = 1,0
Sd = 1,032 m/s2
T = 1,171 s
Shear span ratio of pier S14 a = 14/3,5 = 4 > 3 => q =3,5

## Slide 10
Seismic force in the longitudinal direction
F = M Sd = 5035∙1,032 = 5196 kN
Shear forces in piers
Bending moments in piers
Ms14 = Fs14 hs14 = 2256∙14 = 31584 kNm
Ms21 = Fs21 hs21 = 685 ∙21 = 14385 kNm

## Slide 11
Seismic analysis in the transverse direction
Fundamental mode method – Flexible deck model (FMM)
Structure is subjected to forces Fi = Mi ∙g
Masses are concentrated in nodes at the equidistant lengths of 5m
Half of the mass of piers is added at relevant nodes
75t
75t
5 x150 t
9 x150 t
9 x150 t
217,2 t
217,2 t
250,8 t
5 x150 t

## Slide 12
735,8
The scheme of the inertial forces Fig = Mig
735,8
5 x 1471,5
9 x 1471,5
2130,7
2130,7
2460,3
5 x1471,5
9 x 1471,5
Displacements di, corresponding to inertial forces Fig
average displacement is 0,135m, maximum difference is 0,0270 m
Ratio 0,027/0,135 = 0,20 – the rigid deck model can be used, however this is the maximum allowed value, therefore the analysis is contnued with flexible model
Table 1
node
node

## Slide 13
Using data in Table 1 the following data are obtained:
Period of vibration
Design acceleration
Inertial forces Fi
Table 2
node
node

## Slide 14
Using programme SAP 2000 the following internal forces in piers are calculated
Bending moments
Ms14 = 47710 kNm
Ms21 = 28247 kNm
Shear forces
Vs14 = 3408 kN
Vs21 = 1345 kN
In some cases (e.g. in bridges supported by very short coulmns located near the centre of the brdidge) the method can give unrealistic results
Thus an additional control, presented on the next slide, is performed

## Slide 15
Displacements di (Table 1), corresponding to inertial forces Fig = Mig are divided by the ratio Sd(T) and g
Sd(T)/g = 1,629 / 9,81 = 0,166
Displacements from Table 3 are compared with displacements di1, corresponding to forces Fi (see Table 2)
Table 3 displacements di,0
Table 4 displacements di,1
node
node
node
node

## Slide 16
Displacements from Table 3 and 4
Differences between di,0 in di,1
di,1 (Table 4)
di,0 (Table 3)
Station [m]
Station [m]
Displacement [cm]
Differences [cm]

## Slide 17
1. Area Pd, corresponding to displacements di,1 is calculated 2. Area PD, corresponding to differences between di,1 in di,0 is calculated 3. Pd and PD are compared.
Areas Pd and PD.are calculated as it is illustrated in the following Figure
If PD/Pd < 20%, the results of Fundamental mode method are acceptable. Otherwise the response spectrum analysis should be used.
For the analyzed bridge
Pd = 3,168 m2
PD = 0,161 m2
PD/Pd = 4,4% < 10% regular structure – FMM can be used.
di,1l
di,1d
l

## Slide 18
In EC8/2 it is required to take into account the torsional effects when FMM is used.
Mt = F e, where F is seismic force, e eccentricity
In the analyzed bridge F = SFi = 8149 kN (sum of the forces from Table 2)
e = e0 + ea = 0 + 0,05 L = 0,05 160 = 8 m
L is the length of the bridge
Mt = 8149∙8 = 65192 kNm
This moment is divided to columns supposing the rigid deck, as it is demonstrated in the following slide

## Slide 19
S14
S21
S14
Mt
DFs14
DFs14
100 m
DFS14 = 65192 /100 = 652 kN
Final values of internal forces in S14 are
FS14 = 3408 + 652 = 4060 kN
MS14 = Fs14 x Hs = 4060 x 14 = 56840 kNm
These forces are not considered in the further design, since the Response spectrum analysis (presented in the following slides) results in smaller demand, because the accidental eccentricity ea should not be taken into account (only in very short and skewed bridges)

## Slide 20
Response spectrum method (RSM)
In general the programme is needed to define the fundamental modes of vibration.
Modes of vibrations
T = 1,170 s
T = 0,747 s
meff = 100 %
meff = 95 % - translation in the transverse direction
meff = 71,5% - torsion
mode
1. Mode in the longitudinal direction
2. mode
1. Mode in the transverse direction
3. mode
Torsional mode – rotations around vertical axis
T = 0,736 s
meff = 24,6 % - torsional mode
Note: Torsional mode is not activated, since the structure is symmetric and the masses are symmetric

## Slide 21
In each direction Smeff should be at least 90% of the total mass
Comparison of the periods of vibrations defined by FMM and RSM
Longitudinal direction
FMM RSM
T = 1,171 s T = 1,170 s
Transverse direction
FMM RSM
T = 0,742 s T = 0,747 s

## Slide 22
Spectral accelerations Sd(T) corresponding to each mode of vibration are defined
Internal forces and displacements due to the each mode of vibration are defined
Contributions of different modes are combined using SRSS or CQC rule.
Shear forces in piers, defined using FMM and RSM
Longitudinal direction FMM (without torsion) RSM Difference
Vs14 = 2256 kN Vs14 = 2261 kN 0,22 %
Vs21 = 685 kN Vs21 = 688 kN 0,44 %
Transverse direction
FMM (without torsion) RSM
Vs14 = 3408 kN Vs14 = 3256 kN 4,7%
Vs21 = 1345 kN Vs21 = 1408 kN 4,7%

## Slide 23
Displacements due to the seismic action
Effective stiffness (cross-section) of RC elements should be taken into account.
Effective moment of inertia Ieff can be defined according to Annex C
Approximation of curvature Fy in rectangular cross-sections
MRd – design flexural strength
Fy – yield curvature
esy – yield strain of the reinforcement
ecy – concrete compressive strain corresponding to yielding of the reinforcement
ds - effective depth of the cross-section

## Slide 24
esy
ecy
ds
To define the effective stiffness the design flexural strength MRd (flexural reinforcement) should be known.
If the effective stiffness are used only to calculate the displacements, the flexural reinforcement in columns should be defined prior to the estimation of displacements.
If the seismic forces are also estimated based on the effective stiffness, MRd should be assumed. The assumption should be checked at the end of the analysis.
N

## Slide 25
y1
M
F
x
F
y
y2
M
y1
M
y2
M
F
x
F
x
F
y
F
y
x
y
y1
M
y1
M
F
x
F
y
F
x
F
y
Fy
y
Fy
y
y
Fy
y
Fx
y
y
M
M
M
M
M
M
2
2
2
1
1
1
+
=
+
=
Fy
y
Fy
y
y
Fy
y
Fx
y
y
M
M
M
M
M
M
2
2
2
1
1
1
+
=
+
=
Seismic action in the direction x
Seismic action in the direction y
y2
M
y2
M
y1
M
y1
M
y2
M
y2
M
F
x
F
x
F
y
F
y
x
y
Bridge
Plan view

## Slide 26
100% My
30% Mx
30% My
100% Mx
Bi-axial bending should be taken into account when the flexural reinforcement of piers is defined

## Slide 27
Estimation of the effective stiffness
The flexural reinforcement in piers is defined first
Results of RSM are considered
Pier S14
The basement of the pier
Transverse direction
N = 14329 kN (axial force due to the dead load)
My = 45582 kNm
Mz = 9496 kNm (30% of the bending moment in the longitudinal direction)
Longitudinal direction
N = 14329 kN (axial force due to the dead load)
My = 13675 kNm (30% of the bending moment in the transverse direction)
Mz = 31654 kNm

## Slide 28: Interaction diagram – uniaxial bending

## Slide 29: Interaction diagram – bi-axial bending (Mz-My-N)

## Slide 30
MRd,z = 33500 kNm
MRd,y = 56500 kNm
7
7

## Slide 31
Effective moment of inertia
Results of RSM are taken into account
Pier S14
Transverse direction Longitudinal direction
Shear areas are also appropriatelly reduced

## Slide 32
Pier S21
The basement of the pier
Transverse direction
N = 17485 kN (axial force due to the dead load)
My = 29567 kNm
Mz = 4332 kNm (30% of the bending moment in the longitudinal direction)
Longitudinal direction
N = 17485 kN (axial force due to the dead load)
My = 8870 kNm (30% of the bending moment in the transverse direction)
Mz = 14440 kNm

## Slide 33
MRd,z = 20800 kNm
MRd,y = 34800 kNm
Note:
In EC8/1minimum flexural reinforcement in columns amounts to 1%. The response of hollow box cross-sections is similar to that of the walls. Therefore, the minimum flexural reinforcement of 0,5% was taken into account. This is the minimum reinforcement required in flanges of the walls with limited ductile response - EC8/1

## Slide 34
Effective moment of inertia
Results of RSM are taken into account
Pier S21
Transverse direction Longitudinal direction
Shear areas are also appropriatelly reduced

## Slide 36
Analysis is repeated taking into account estimated effective stiffness
Periods of vibrations corresponding to the effective stiffness
T1 = 2,355 s meff = 100%
T2 = 1,376 s meff = 99,6% (meff = 75% - zasuki okoli z osi)
T3 = 1,288 s meff = 25% (zasuki okoli z osi)
Displacements above the abutments:
Displacements corresponding to the reduced seismic action
Longitudinal direction
dEe,long = 6,12 cm (T1 > 2s displacements are defined based on the elastic spectrum)
Transverse direction
dEe,tran = 3,80 cm
Displacements due to the seismic action:
Longitudinal direction
Transverse direction

## Slide 37
Ragularity of the bridge
r = q MEd / MRd
In piers S14 r = q = 3,5, since the flexural strength is fully exploited
Pier S21 can be neglected, since its contribution to total base shear is less than 20%
Longitudinal direction
VES,21 = 688 Vtot = 5210 VES,21/Vtot = 688 / 5210 = 0,132
Transverse direction
VES,21 = 1408 Vtot = 7920 VES,21/Vtot = 1408 / 7920 = 0,178
rmax = rmin => r = 1 < ro = 2 bridge is regular

## Slide 38
The presented procedure, used to estimate the seismic action effects in terms of forces is conservtive
They can be also estimated considering the effective stiffness
To estimate the effective stiffness the flexural strength MRd (flexural reinforcement) should be assumed
According to EC8/1 the effective stiffness can be estimated reducing the stiffness corresponding to the gross cross-sections by 50%. Thus the moments of inertia and shear areas corresponding to gross cross-sections were reduced by 50%.
The corresponding periods of vibrations were
T1 = 1,654 s meff = 100%
T2 = 1,038 s meff = 99,5% (meff = 74,9% - torsion)
T3 = 1,014 s meff = 24,7% (torsion)

## Slide 39
Internal forces in piers
Pier S14
Internal forces at the basement
Transverse direction
N = 14329 kN (axial force due to the dead load)
My = 34771 kNm
Mz = 6713 kNm (30% of the bending moment in the longitudinal direction)
Longitudinal direction
N = 14329 kN (axial force due to the dead load)
My = 10431 kNm (30% of the bending moment in the transverse direction)
Mz = 22377 kNm

## Slide 40
Internal forces in piers
Pier S21
Internal forces at the basement
Transverse direction
N = 17485 kN (axial force due to the dead load)
My = 18494 kNm
Mz = 3059 kNm (30% of the bending moment in the longitudinal direction)
Longitudinal direction
N = 17485 kN (axial force due to the dead load)
My = 5548 kNm (30% of the bending moment in the transverse direction)
Mz = 10197 kNm

## Slide 41
Flexural reinforcement in pier S14
MRd,y = 41500 kNm
MRd,z = 25000 kNm

## Slide 42
Effective moments of inertia
Pier S14
Transverse direction Longitudinal direction
Shear areas are also appropriatelly reduced

## Slide 43
MRd,y = 34800 kNm
MRd,z = 20800 kNm
Flexural reinforcement in pier S21

## Slide 44
Effective moments of inertia
Pier S21
Transverse direction Longitudinal direction
Shear areas are also appropriatelly reduced

## Slide 45
The effective stiffness of pier S14 is smaller than that assumed at the begining of the analysis. Estimated forces are still conservative. Displacements should be estimated based on the reduced effective stiffness.
The effective stiffness of Pier S21 is also smaller than the assumed value.
However it is not clear that the estimated effective stiffness will be actually activated since the provided strength is larger from the required value (minimum reinforcement is provided). Therefore, the reduction of the effective stiffness larger than 50% can not be taken into account for the estimation of forces. For the estimation of displacements the larger reduction of the effective stiffness can be taken into account since the results are conservative.

## Slide 46
Displacements (estimated reduction of the effective stiffness was considered)
Periods of vibrations
T1 = 2,642 s
T2 = 1,646 s
T3 = 1,557 s
Displacements above the abutments dEe due to the reduced seismic action
Longitudinal direction
dEe = 6,12 cm (elastic spectrum was considered)
Transverse direction
dEe = 4,82 cm
Diasplacaments due to the seismic action
Longitudinal direction
dE = dEe∙q = 6,4 ∙3,5 = 21,4 cm
Transverse direction
dE = dEe∙q = 4,82∙3,5 = 16,9 cm

## Slide 47
Comparison of the two approaches
Periods of vibrations
Unreduced effective stiffness (forces) Reduced effective stiffness (50%)
T1 = 1,170 s T1 = 1,654 s
T2 = 0,747 s T2 = 1,038 s
Flexural reinforcement
Unreduced effective stiffness (forces) Reduced effective stiffness (50%) S14 m = 1,86% S14 m = 1,01%
S21 m = 0,50% (minimum) S21 m = 0,50% (minimum)
Displacements (reduced eff. stiffness) Displacements (reduced eff. stiffness)
de,long = 21,4 cm de,long = 21,4 cm
de,tran = 13,3 cm de,tran = 16,9 cm

## Slide 48
Displacements due to the other actions
Displacements due to the seismic action should be combined with displacements due to the other actions: a) displacements dG due to the permanent and quasi-permanent actions (e.g. pre-stressing, creep, shrinkage)
b) Due to the quasi-permanent temperature effects y2dT

## Slide 49
Detailing
Flexural strength at the basement
Overstrength factor go
Pier S14
Pier S21
Opomba:
Normalized axial force is less than 0,2; Special confinement reinforcement is not required 6.2.4(4)
Therefore, the overstrength factor amounts to 1,35

## Slide 50
Flexural strength at the basement
Pier S14
Transverse direction
MRd = 56500 kNm
Mo = g0 MRd = 1,35∙56500 = 76275 kNm
Longitudinal direction
MRd = 33500 kNm
Mo = g0 MRd = 1,35∙33500 = 45225 kNm
Pier S21
Transverse direction
MRd = 34800 kNm
Mo = g0 MRd = 1,35∙34800 = 46980 kNm
Longitudinal direction
MRd = 20800 kNm
Mo = g0 MRd = 1,35∙20800 = 28080 kNm

## Slide 51
Plastic hinge length and the flexural reinforcement outside the plastic hinge region
Bending moments that were taken into account to define the flexural reinforcement outside the plastic hinge region
MRd
Mo = 1,35·MRd
Lp = 0,26Hs
Hs – height of the column
Minimum plastic hinge length:
0,2 Hs or depth of the cross-section in the relevant direction (larger value)
In the analyzed bridge the minimum length of the plastic hinge is Lp = 3,5m
In pier S14 Lp is:
Lp = 0,26 ·1400 = 364 cm
In pier S21 Lp is:
Lp = 0,26 ·2100 = 546 cm
Capacity design bending moments outside the Lp

## Slide 52
Maximum bending moments outside the plastic hinge region:
Pier S14
Transverse direction
My = 56500 kNm (NG = 13987 kN)
Longitudinal direction
Mz = 33500 kNm (NG = 13987 kN)
Pier S21
Transverse direction
My = 34800 kNm (NG = 16972 kN)
Longitudinal direction
Mz = 20800 kNm (NG = 16972 kN)

## Slide 53
7
7
Pier S14

## Slide 54
Pier S21
Minimum reinforcement
along the total height of pier S21

## Slide 55
At the top 5,7 m of S14 minimum reinforcement provides adequate flexural strength
NG = 13548 kN
My = 5,7 / 14 x 76275 = 31050 kNm
Mz = 5,7 / 14 x 45225 = 18410 kNm

## Slide 56
Shear reinforcement at the plastic hinge region
Calculated based on the maximum shear forces Vc
In cantilever columns it is defined as:
Pier S14 Transverse
Longitudinal
Pier S21
Transverse
Longitudinal

## Slide 57: Different shear mechanisms of concrete without shear reinforcement
Arch mechanism
Truss
Concrete shear mechanisms:
friction
dowel
compression zone

## Slide 58: Shear failure modes
Arch failure
Compression diagonal failure
Exceeded principal tension stresses
Failure of the truss mechanism
(e) Sliding failure –short piers
(e)

## Slide 59
First the shear strength of the concrete without shear reinforcement is checked
Shear strength of concrete in pier S14
CRd,c = 0,18/1,5 = 0,12
k1=0,15
NEd =14329kN
Ac = 3,76
fck = 25MPa

## Slide 60
Transverse direction
Longitudinal direction
VRd,max = 0,5bwdnfcd = 0,5 0,696 3,103 0,54 16,7 1000 = 9738 kN > 5448 kN

## Slide 61
Total shear force should be sustained by the shear reinforcement
Transverse direction
Longitudinal direction
4 legs stirrups f12/10cm

## Slide 62
Transverse direction
Longitudinal direction
Shear strength of concrete in pier S21

## Slide 63
Total shear force is sustained by the shear reinforcement
Transverse direction
Longitudinal direction
4 leg stirrups f8/10cm

## Slide 64
Buckling of the longitudinal reinforcement
Two possible failure modes
Large distance between stirrups Small amount of the transverse reinforcement

## Slide 65
Maximum distance between stirrups
sL = d f
d = 2,5(ftk / fyk) + 2,25 = 2,5 1,35 + 2,25 = 5,625
sL = 5,625 2,2 = 12,4 cm
Pier S14
sL = d f
d = 2,5(ftk / fyk) + 2,25 = 2,5 1,35 + 2,25 = 5,625
sL = 5,625 1,4 = 7,9 cm
Pier S21
ftk – tensile strength of the transverse reinforcement
fyk – yield strength of the transverse reinforcement

## Slide 66
Maximum distance between stirrups legs (the procedure is not correct, will be changed in new version of EC8/2)
Pier S14
Pier S21
sl
sl
sl
sl

## Slide 67
Summary of the reinforcement
Pier S14
m = 1,86%
m = 0,5%
8,3 m
5,7 m
f12/10
Shear reinforcement

## Slide 68
Summary of the reinforcement
Pier S21
= 0,5%
Minimum reinforcement
5,46 m
f8/10
Shear reinforcement
f8/7,5
Buckling

## Slide 69
Capacity design:
Superstructure
Bearings
Foundations
Abutments