## Slide 1: DESIGN OF EARTHQUAKE RESISTANT BRIDGES ACCORDING TO EUROCODE 8-2
T. Isaković
UNIVERSITY OF LJUBLJANA
Faculty of Civil and Geodetic Engineering

## Slide 2: Observations from past earthquakes
Reinforced concrete piers – insufficient transverse reinforcement
Deficient shear strength
  Inadequate confinement reinforcement
  Buckling of the longitudinal reinforcement
  Longitudinal reinforcement overlapped at the critical regions
Steel piers
Brittle failure
  Buckling of piers

## Slide 3: Deficient shear strength

## Slide 4: Inadequate confinement reinforcement

## Slide 5: Overlapping of the longitudinal reinforcement in the critical regions

## Slide 6: Buckling of the longitudinal reinforcement

## Slide 7: Steel piers – brittle failure

## Slide 8: Steel piers - Buckling

## Slide 9: Inadequate seating lengths

## Slide 10: Modern standards – better safety

## Slide 11: Basic features of EC8/2
I. Explicit reduction of the seismic action
II. Reduction of the seismic action is defined based on the intended type of the response (ductile or limited ductile response)
III. Capacity design
IV. Detailing, which provides the foreseen type of response
V. Control of displacements

## Slide 12: I. Explicit reduction of seismic forces
displacement
force
Ductile response
Limited ductile response
Ideal elastic response
Essentially elastic response

## Slide 13: Elastic acceleration spectrum

## Slide 14
Type of the soil

## Slide 16
Ductility
Ductility is the ability of the material, the element or the structure to undergo significant inelastic deformations before the failure
ductile
brittle
Generalized force
Generalized deformation

## Slide 17
Du – ultimate generalized deformation
Dy – yield generalized deformation

## Slide 18: Parameters that influence the ductility of the cross-section
Axial force
Tensile and compression reinforcement
Compression zone
Compression strength of concrete
Amount of transverse reinforcement

## Slide 19: Larger axial forces – lower ductility

## Slide 20: Amount and the type of tensile reinforcement

## Slide 21: Class of concrete

## Slide 22
Confined concrete
unconfined concrete

## Slide 23: Behaviour factor q– reduction of the seismic action
Depends on the foreesen type of the response
  Ductile or limited ductile
Depends on the type of elements where the energy is dissipated

## Slide 24: II. Values of behaviour factors - q

## Slide 25: II. Maximum values of behaviour factors q
In regular ductile bridges
Regularity should be explicitely checked

## Slide 26: II. Regularity
Local reduction factor
r0 = 2

## Slide 27: II. Large compression stresses
h
k
> 0,6
qr = 1

## Slide 28: II. Short columns – lower ductility
as = L/h
qr = q as
h
L

## Slide 29: III. Capacity design
Brittle types of failure should be prevented

## Slide 30: III. Capacity design - column
V
C,O
= M
O
/h
M
O
=
g
O
M
Rd
h
MRd
Lh
Lh – plastic hinge region
MC

## Slide 31
Top displacement d
C
A
B
d
p
Shear force
Shear strength
Shear failure

## Slide 32: III. Shear strength – plastic hinge region
According to EC2; strength VRd,c, VRd,s in VRd,max is reduced by factor
If max VC is larger than VRd,c shear force should be sustained by shear reinforcement
Alternative 1
Alternative 2

## Slide 33: III. Capacity design - structure
V
C,O
= M
O
/h
M
O
=
g
O
M
Rd
V
C,O
= M
O
/h
h
actions on fundation
action on bearing
VC,0 – maximum possible shear force in column:
calculated based on the flexural capacity of the column (taking into account an ovrestrength)

## Slide 34: IV. Confinement reinforcement - details
Typical confinement details

## Slide 35: IV. Confinement reinforcement – plastic hinge region
Mechanical reinforcement ratio
Rectangular cross-sections Circular cross-sections
Dimensions of the concrete core – between stirrups

## Slide 36: IV. Required confinement reinforcement
Rectangular cross-sections
Circular cross-sections
In each direction

## Slide 37: IV. Minimum confinement reinforcement

## Slide 38: IV. Transverse reinforcement that secure column against buckling of compression longitudinal reinforcement
sL
Maximum distance in longitudinal direction of column – sL = 5-6 flong.
sL

## Slide 39: V. Displacements due to the seismic action
Reduced seismic action: displacements dEe
Actual displacements
Long periods of vibration T > 1.25 TC
Short periods of vibration

## Slide 40: V. Estimation of displacements
Iterative – effective cross-section
Based on the assumed design strength MRd
This assumption should be checked after the analysis
If required MRd,req is less than the assumed value, displacements are multiplied by MRd/MRd,req.
If MRd,req is larger, the analysis should be repeated, seismic demand is larger

## Slide 41
Annex C – Method 2
esy
ecy
N
dS
(
)
s
sy
y
s
cy
sy
y
y
Rd
eff
c
d
d
M
I
E
/
1
,
2
2
,
1
e
e
e
=
F
-
=
F
F
=
F
y
can be estimated as (rectangular cross-sections)
M
Rd
–
Design flexural strength
F
y
–
Yield curvature
e
sy
–
Yield strain of the reinforcement
e
cy
–
Compressive strain of concrete
d
s
-
Effective depth of the cross-section

## Slide 42: Methods of analysis
Elastic methods of analysis
  Response spectrum method: reference method (RSM)
  Fundamental mode method (FMM)
Nonlinear methods of analysis
- Simplified pushover based analysis – N2 method
- Dynamic nonlinear response history analysis (NRHA)
Nonlinear methods of analysis cannot be used to relax the results of elastic methods of analysis

## Slide 43
Appendix:
Bridge Design Example according to EC8-2

## Slide 44: EC8/2 versus former design practice
Bridge
Flexural reinforcement
Transverse reinforcement
EC8
As built
EC8
As built
* bridge was designed taking into account modern sesimic design philosophy

## Slide 45: Existing bridges with substandard details
Eurocode 8-2 regulates mainly the design of new bridges
Eurocode 8-3 regulates the seismic assessment and strengthening of existing buildings

## Slide 46: EC8 – 3: Methods of analysis
Elastic analysis considering the reduced design acceleration spectrum (q = 1,5)
Elastic analysis considering the elastic (unreduced) acceleration spectrum
Non-linear analysis (static or dynamic)

## Slide 47: Strengthening
Depends on the type of deficiencies
Increasing resistance
  Strengthening of columns using concrete, steel or FRP jacketing

## Slide 48: Strengthening
Reducing demand
  Base isolation and the increase of damping – high-damping rubber bearings (damping 15 % - 20%), dampers

## Slide 49: An example of the increased strength

## Slide 50
Experiments (Scale 1:4)
Assessment of as-built columns

## Slide 51
Response of as-built short column

## Slide 52: The increase of resistance – concrete jacketing

## Slide 53
Response of as-built and strengthened short column

## Slide 55: The increase of resistance – FRP jacketing

## Slide 56
Response of as-built and strengthened short column
FRP
Concrete

## Slide 57: FRP jacketing

## Slide 58: FRP jacketing

## Slide 59: FRP jacketing

## Slide 60: Presstresed FRP jacket

## Slide 61: Presstresed FRP jacket

## Slide 62: Conclusions
Explicit reduction of seismic forces
Reduction of the initial stiffness
Capacity design
Conservative estimation of the shear capacity
Structural details providing adequate confinement of critical zones and preventing buckling of longitudinal bars
Existing bridges – do not explicitly cover
EC8-3 and EC8-2 can be applied